## Slide 1: Computational Photography lecture 10 – (pinhole) stereo cameras CS 590-134 (future 572) Spring 2016
Prof. Alex Berg
(Credits to many other folks on individual slides)

## Slide 2
Assignment 2 – part II due Monday Sept 29 at midnight
Today, talking about making (pinhole (stereo)) cameras
Re-read Chapter 2 in the Szeliski book as reference material
Also look at chapter 11 on stereo!
Today
Notes: (votes and comments are their votes for the best homework 1 write-up, and the best image in any of the write-ups.) Sakai should be open by the time class happens. I am working to try and combine the sakai for 590 and 790, hopefully this will work out 

## Slide 3
“I made my first picture using camera obscura techniques in my darkened living room in 1991.”
-- Abelardo Morell
I cover all windows with black plastic in order to achieve total darkness.”
-- Abelardo Morell
“In setting up a room to make this kind of photograph,

## Slide 4
“I made my first picture using camera obscura techniques in my darkened living room in 1991.”
-- Abelardo Morell
I cover all windows with black plastic in order to achieve total darkness.”
-- Abelardo Morell
“In setting up a room to make this kind of photograph,

## Slide 5: Next assignment: Making pinhole cameras (and stereo depth estimation)
Groups of 1-2 – find a partner with a good digital camera
http://en.wikipedia.org/wiki/Anaglyph_3D
From James Hays
Based on a class project from Antonio Torralba’s Vision class (MIT).

## Slide 6: Stereo and Depth Estimation (Sz 11)
cs129: Computational Photography
James Hays, Brown, Spring 2011
Slides from Steve Seitz and Robert Collins

## Slide 7: How is depth estimated?

## Slide 8: Time of Flight
Humans can learn to echolocate!

## Slide 12: Stereo Vision
Not that important for humans, especially at longer distances. Perhaps 10% of people are stereo blind.
Many animals don’t have much stereo overlap in their fields of view

## Slide 13
Public Library, Stereoscopic Looking Room, Chicago, by Phillips, 1923

## Slide 14
Teesta suspension bridge-Darjeeling, India

## Slide 15
Woman getting eye exam during immigration procedure at Ellis Island, c. 1905 - 1920 , UCR Museum of Phography

## Slide 16
Mark Twain at Pool Table", no date, UCR Museum of Photography

## Slide 17
San Francisco Post-Earthquake 1906
http://www.sfog.us/earthquake

## Slide 18
San Francisco Post-Earthquake 1906
http://www.sfog.us/earthquake

## Slide 24: Stereo
scene point
optical center
image plane

## Slide 25: Stereo
Basic Principle: Triangulation
  Gives reconstruction as intersection of two rays
  Requires
    camera pose (calibration)
    point correspondence

## Slide 26: Stereo correspondence
Determine Pixel Correspondence
  Pairs of points that correspond to same scene point
Epipolar Constraint
  Reduces correspondence problem to 1D search along conjugate epipolar lines
epipolar plane
epipolar line
epipolar line

## Slide 27: Fundamental matrix
Let p be a point in left image, p’ in right image
Epipolar relation
  p maps to epipolar line l’
  p’ maps to epipolar line l
Epipolar mapping described by a 3x3 matrix F
It follows that
l’
l
p
p’

## Slide 28: Fundamental matrix
This matrix F is called
  the “Essential Matrix”
    when image intrinsic parameters are known
  the “Fundamental Matrix”
    more generally (uncalibrated case)
Can solve for F from point correspondences
  Each (p, p’) pair gives one linear equation in entries of F
  8 points give enough to solve for F (8-point algorithm)
  see Marc Pollefey’s notes for a nice tutorial

## Slide 29: Stereo image rectification

## Slide 30: Stereo image rectification
reproject image planes onto a common
plane parallel to the line between optical centers
pixel motion is horizontal after this transformation
two homographies (3x3 transform), one for each input image reprojection
C. Loop and Z. Zhang. Computing Rectifying Homographies for Stereo Vision. IEEE Conf. Computer Vision and Pattern Recognition, 1999.

## Slide 31: Stereo matching algorithms
Match Pixels in Conjugate Epipolar Lines
  Assume brightness constancy
  This is a tough problem
  Numerous approaches
    A good survey and evaluation: http://www.middlebury.edu/stereo/

## Slide 32: Your basic stereo algorithm
For each epipolar line
For each pixel in the left image
    compare with every pixel on same epipolar line in right image
    pick pixel with minimum match cost
Improvement: match windows
  This should look familar...

## Slide 33: Window size
  Smaller window
  Larger window
W = 3
W = 20
Better results with adaptive window
  T. Kanade and M. Okutomi, A Stereo Matching Algorithm with an Adaptive Window: Theory and Experiment,, Proc. International Conference on Robotics and Automation, 1991.
  D. Scharstein and R. Szeliski. Stereo matching with nonlinear diffusion. International Journal of Computer Vision, 28(2):155-174, July 1998
Effect of window size
Notes: smaller window: more detail, more noise
bigger window: less noise, more detail

## Slide 34: Stereo results
Ground truth
Scene
  Data from University of Tsukuba
  Similar results on other images without ground truth

## Slide 35: Results with window search
Window-based matching
(best window size)
Ground truth

## Slide 36: Better methods exist...
Better Method
  Boykov et al., Fast Approximate Energy Minimization via Graph Cuts,
  International Conference on Computer Vision, September 1999.
Ground truth
    For the latest and greatest: http://www.middlebury.edu/stereo/

## Slide 37: Stereo as energy minimization
What defines a good stereo correspondence?
  Match quality
    Want each pixel to find a good match in the other image
  Smoothness
    If two pixels are adjacent, they should (usually) move about the same amount

## Slide 38: Stereo as energy minimization
Expressing this mathematically
  Match quality
    Want each pixel to find a good match in the other image
  Smoothness
    If two pixels are adjacent, they should (usually) move about the same amount
We want to minimize
  This is a special type of energy function known as an MRF (Markov Random Field)
    Effective and fast algorithms have been recently developed:
      Graph cuts, belief propagation….
      for more details (and code): http://vision.middlebury.edu/MRF/
      Great tutorials available online (including video of talks)

## Slide 39: Depth from disparity
f
x
x’
baseline
z
C
C’
X
f

## Slide 41: Stereo reconstruction pipeline
  Camera calibration errors
  Poor image resolution
  Occlusions
  Violations of brightness constancy (specular reflections)
  Large motions
  Low-contrast image regions
Steps
  Calibrate cameras
  Rectify images
  Compute disparity
  Estimate depth
What will cause errors?

## Slide 42: Active stereo with structured light
Project “structured” light patterns onto the object
  simplifies the correspondence problem
camera 2
camera 1
projector
camera 1
projector
Li Zhang’s one-shot stereo

## Slide 43: Active stereo with structured light

## Slide 44: Laser scanning
Optical triangulation
  Project a single stripe of laser light
  Scan it across the surface of the object
  This is a very precise version of structured light scanning
Digital Michelangelo Project
http://graphics.stanford.edu/projects/mich/

## Slide 45: Laser scanned models
  The Digital Michelangelo Project, Levoy et al.

## Slide 46: Laser scanned models
  The Digital Michelangelo Project, Levoy et al.

## Slide 47: Laser scanned models
  The Digital Michelangelo Project, Levoy et al.

## Slide 48: Laser scanned models
  The Digital Michelangelo Project, Levoy et al.

## Slide 49: Laser scanned models
  The Digital Michelangelo Project, Levoy et al.