## Slide 1: Computational Photography Lecture 6 – Matching Keypoints CS 590-134 (Future 572) Spring 2016
Prof. Alex Berg
Special Guest Lecture Prof. Enrique Dunn
(Credits to many other folks on individual slides)

## Slide 2
Today
Delving into how to match local features in order to align images with more general transformations than translation. Part 1
Notes: (votes and comments are their votes for the best homework 1 write-up, and the best image in any of the write-ups.) Sakai should be open by the time class happens. I am working to try and combine the sakai for 590 and 790, hopefully this will work out 

## Slide 3
Many slides from Derek Hoiem, Kristen Grauman, Bastian Leibe

## Slide 4: Pinhole camera projections
“Linear” projection from 3D to 2D
  projection matrix depends on focal length, principal point, etc.
Camera Center
(tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u

## Slide 5: Vanishing points and metrology
Parallel lines in 3D intersect at a vanishing point in the image
Can measure relative object heights using vanishing point tricks
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)
1
2
3
4
5

## Slide 6: Single-view 3D Reconstruction
Technically impossible to go from 2D to 3D, but we can do it with simplifying models
  Need some interaction or recognition algorithms
  Uses basic VP tricks and projective geometry

## Slide 7: Lens, aperture, focal length
Aperture size and focal length control amount of exposure needed, depth of field, field of view
Good explanation: http://www.cambridgeincolour.com/tutorials/depth-of-field.htm

## Slide 8: Capturing light with a mirrored sphere

## Slide 9: One small snag
How do we deal with light sources? Sun, lights, etc?
  They are much, much brighter than the rest of the environment
Use High Dynamic Range photography!
1
46
1907
15116
18
.
.
.
.
.
Relative Brightness

## Slide 10: Key ideas for Image-based Lighting
Capturing HDR images: needed so that light probes capture full range of radiance

## Slide 11: Key ideas for Image-based Lighting
Relighting: environment map acts as light source, substituting for distant scene

## Slide 12: General direction
Correspondence
  How do we find matching patches in two images?
  How can we automatically align two images of the same scene?
  How do we find images with similar content?
  How do we tell if two pictures are of the same person’s face?
  How can we detect objects from a particular category?
Applications
  Photo stitching
  Object recognition
  3D Reconstruction
Notes: We are just looking at the first step in the direction of more general alignment and recognition…

## Slide 13: How can we align two pictures?
Case of global transformation

## Slide 14: How can we align two pictures?
Global matching?
  But what if
    Not just translation change, but rotation and scale?
    Only small pieces of the pictures match?

## Slide 15: Today: Keypoint Matching
B1
B2
B3
A1
A2
A3
1. Find a set of distinctive key- points
3. Extract and normalize the region content
2. Define a region around each keypoint
4. Compute a local descriptor from the normalized region
5. Match local descriptors

## Slide 16: Main challenges
Change in position, scale, and rotation
Change in viewpoint
Occlusion
Articulation, change in appearance

## Slide 17: Question
Why not just take every patch in the original image and find best match in second image?
Notes: Too many patches, do you have to search over scale and rotation too? Many patches are not distinctive, so their best match might be misleading.

## Slide 18: Goals for Keypoints
Detect points that are repeatable and distinctive

## Slide 19: Key trade-offs
More Points
More Repeatable
B1
B2
B3
A1
A2
A3
Localization
More Robust
More Selective
Description
Robust to occlusion
Works with less texture
Robust detection
Precise localization
Deal with expected variations
Maximize correct matches
Minimize wrong matches

## Slide 20: Keypoint localization
Suppose you have to click on some point, go away and come back after I deform the image, and click on the same points again.
  Which points would you choose?
original
deformed

## Slide 21: Keypoint Localization
Goals:
  Repeatable detection
  Precise localization
  Interesting content

## Slide 22: Choosing interest points
Where would you tell your friend to meet you?
Notes: Corners!

## Slide 23: Choosing interest points
Where would you tell your friend to meet you?
Notes: Blobs!

## Slide 24: Choosing interest points
Corners
Peaks/Valleys

## Slide 25: Which patches are easier to match?
?

## Slide 26: Choosing interest points
If you wanted to meet a friend would you say
  “Let’s meet on campus.”
  “Let’s meet on Green street.”
  “Let’s meet at Green and Wright.”
Or if you were in a secluded area:
  “Let’s meet in the Plains of Akbar.”
  “Let’s meet on the side of Mt. Doom.”
  “Let’s meet on top of Mt. Doom.”

## Slide 27: Many Existing Detectors Available
Hessian & Harris [Beaudet ‘78], [Harris ‘88]
Laplacian, DoG [Lindeberg ‘98], [Lowe 1999]
Harris-/Hessian-Laplace [Mikolajczyk & Schmid ‘01]
Harris-/Hessian-Affine [Mikolajczyk & Schmid ‘04]
EBR and IBR [Tuytelaars & Van Gool ‘04]
MSER [Matas ‘02]
Salient Regions [Kadir & Brady ‘01]
Others…

## Slide 28: Harris Detector [Harris88]
Intuition: Search for local neighborhoods where the image changes in two directions, where has two large eigenvalues.
is a two by two matrix
Notes: This formula is a bit complex looking, but Ix is just the change (or derivative) of the image in the x direction, and Iy is the derivative in the y direction. These are summed up over a local window, and in this version the sum is weighted by a gaussian, g, so that the vaues in the middle of the window count more.
The eigenvalues of the matrix mu (mew) at some point tell you something about the shape of the intensity pattern. If both eigenvalues are small, there isn‘t much change in the image. If one eigenvalue is small, and the other is big, there is only change in one direction, and if both are large there is change in both directions, and it might be a good feature point, like a corner.
Alex thinks it might be nice for you to try to verify this yourself by going over the calculations on a piece of paper sometime...

## Slide 29: Harris Detector [Harris88]
Second moment matrix
1. Image derivatives
2. Square of derivatives
3. Gaussian filter g(sI)
Ix
Iy
Ix2
Iy2
IxIy
g(Ix2)
g(Iy2)
g(IxIy)
4. Cornerness function – both eigenvalues are strong
har
5. Non-maxima suppression
g(IxIy)
Notes: One trick for deciding if both eigenvalues are large is to look at the difference between the determinant and the trace.

## Slide 30: Matlab code for Harris Detector
function [ptx, pty] = detectKeypoints(im, alpha, N)
% get harris function
gfil = fspecial('gaussian', [7 7], 1); % smoothing filter
imblur = imfilter(im, gfil); % smooth image
[Ix, Iy] = gradient(imblur); % compute gradient
Ixx = imfilter(Ix.*Ix, gfil); % compute smoothed x-gradient sq
Iyy = imfilter(Iy.*Iy, gfil); % compute smoothed y-gradient sq
Ixy = imfilter(Ix.*Iy, gfil);
har = Ixx.*Iyy - Ixy.*Ixy - alpha*(Ixx+Iyy).^2; % cornerness
% get local maxima within 7x7 window
maxv = ordfilt2(har, 49, ones(7)); % sorts values in each window
maxv2 = ordfilt2(har, 48, ones(7));
ind = find(maxv==har & maxv~=maxv2);
% get top N points
[sv, sind] = sort(har(ind), 'descend');
sind = ind(sind);
[pty, ptx] = ind2sub(size(im), sind(1:min(N, numel(sind))));

## Slide 31: Harris Detector – Responses [Harris88]
Effect: A very precise corner detector.
Notes: Note the points where the detector responds, the corner and the white dots, in the centers, as well.

## Slide 32: Harris Detector – Responses [Harris88]

## Slide 33: So far: can localize in x-y, but not scale

## Slide 34: Automatic Scale Selection
How to find corresponding patch sizes?
Notes: Spend some time explaining the background idea here –define a fucntion of scale around a point so that it has extrema in similar places for two views of a features, where similar places means it selects the same realworld scale if you use the extrema to pick scale.

## Slide 35: Automatic Scale Selection
Function responses for increasing scale (scale signature)

## Slide 36: Automatic Scale Selection
Function responses for increasing scale (scale signature)

## Slide 37: Automatic Scale Selection
Function responses for increasing scale (scale signature)

## Slide 38: Automatic Scale Selection
Function responses for increasing scale (scale signature)

## Slide 39: Automatic Scale Selection
Function responses for increasing scale (scale signature)

## Slide 40: Automatic Scale Selection
Function responses for increasing scale (scale signature)

## Slide 41: What Is A Useful Signature Function?
Difference of Gaussian = “blob” detector

## Slide 42: Difference-of-Gaussian (DoG)
-
=

## Slide 43: DoG – Efficient Computation
Computation in Gaussian scale pyramid
s
Original image
Sampling with step s4 =2
s
s
s

## Slide 44: Results: Lowe’s DoG

## Slide 45: Orientation Normalization
Compute orientation histogram
Select dominant orientation
Normalize: rotate to fixed orientation
0
2
p
[Lowe, SIFT, 1999]

## Slide 46: Available at a web site near you…
For most local feature detectors, executables are available online:
  http://robots.ox.ac.uk/~vgg/research/affine
  http://www.cs.ubc.ca/~lowe/keypoints/
  http://www.vision.ee.ethz.ch/~surf

## Slide 47: How do we describe the keypoint?

## Slide 48: Local Descriptors
The ideal descriptor should be
  Robust
  Distinctive
  Compact
  Efficient
Most available descriptors focus on edge/gradient information
  Capture texture information
  Color rarely used

## Slide 49: Local Descriptors: SIFT Descriptor
[Lowe, ICCV 1999]
Histogram of oriented gradients
Captures important texture information
Robust to small translations / affine deformations
K. Grauman, B. Leibe

## Slide 50: Details of Lowe’s SIFT algorithm
Run DoG detector
  Find maxima in location/scale space
  Remove edge points
Find all major orientations
  Bin orientations into 36 bin histogram
    Weight by gradient magnitude
    Weight by distance to center (Gaussian-weighted mean)
  Return orientations within 0.8 of peak
    Use parabola for better orientation fit
For each (x,y,scale,orientation), create descriptor:
  Sample 16x16 gradient mag. and rel. orientation
  Bin 4x4 samples into 4x4 histograms
  Threshold values to max of 0.2, divide by L2 norm
  Final descriptor: 4x4x8 normalized histograms
Lowe IJCV 2004

## Slide 51: Matching SIFT Descriptors
Nearest neighbor (Euclidean distance)
Threshold ratio of nearest to 2nd nearest descriptor
Lowe IJCV 2004

## Slide 52: Local Descriptors: SURF
Fast approximation of SIFT idea
  Efficient computation by 2D box filters & integral images  6 times faster than SIFT
  Equivalent quality for object identification
[Bay, ECCV’06], [Cornelis, CVGPU’08]
GPU implementation available
  Feature extraction @ 200Hz (detector + descriptor, 640×480 img)
  http://www.vision.ee.ethz.ch/~surf

## Slide 53: What to use when?
Detectors
Harris gives very precise localization but doesn’t predict scale
  Good for some tracking applications
DOG (difference of Gaussian) provides ok localization and scale
  Good for multi-scale or long-range matching
Descriptors
SIFT: good general purpose descriptor

## Slide 54: Things to remember
Keypoint detection: repeatable and distinctive
  Corners, blobs
  Harris, DoG
Descriptors: robust and selective
  SIFT: spatial histograms of gradient orientation

## Slide 55: Future Assignment: Panoramic Stitching
Camera Center