## Slide 1: Computational Photography lecture 7 – (pinhole) cameras CS 590-134 (Future 572) Spring 2016
Prof. Alex Berg
(Credits to many other folks on individual slides)

## Slide 2
Tell me about why and how to find corresponding points…
Will hand back (electronically) your assignments next lecture.
We will talk about using correspondence for next part of assignment,
but first we need to talk about camera geometry and transformations a bit.
Today
Notes: (votes and comments are their votes for the best homework 1 write-up, and the best image in any of the write-ups.) Sakai should be open by the time class happens. I am working to try and combine the sakai for 590 and 790, hopefully this will work out 

## Slide 3: Pinhole Camera Model
Sildes from Derek Hoiem, University of Illinois

## Slide 4: Single-view Geometry
How tall is this woman?
Which ball is closer?
How high is the camera?
What is the camera rotation?
What is the focal length of the camera?

## Slide 5: Some camera concepts
Mapping between image and world coordinates
  Pinhole camera model
  Projective geometry
    Vanishing points and lines
  Projection matrix

## Slide 6: Image formation
Let’s design a camera
  Idea 1: put a piece of film in front of an object
  Do we get a reasonable image?
Slide source: Seitz

## Slide 7: Pinhole camera
Idea 2: add a barrier to block off most of the rays
  This reduces blurring
  The opening known as the aperture
Slide source: Seitz
Notes: Q: How does this transform the image? A: It gets inverted

## Slide 8: Pinhole camera
Figure from Forsyth
f
f = focal length
c = center of the camera
c

## Slide 9: Camera obscura: the pre-camera
First idea: Mo-Ti, China (470BC to 390BC)
First built: Alhacen, Iraq/Egypt (965 to 1039AD)
Illustration of Camera Obscura
Freestanding camera obscura at UNC Chapel Hill
Photo by Seth Ilys

## Slide 10: Camera Obscura used for Tracing
Lens Based Camera Obscura, 1568

## Slide 11: First Photograph
Joseph Niepce, 1826
Photograph of the first photograph
Stored at UT Austin
Oldest surviving photograph
  Took 8 hours on pewter plate
Niepce later teamed up with Daguerre, who eventually created Daguerrotypes

## Slide 12: Pinhole camera
A lens focuses light onto the film
“circle of
confusion”
Slide source: Seitz

## Slide 13: Dimensionality Reduction Machine (3D to 2D)
Figures © Stephen E. Palmer, 2002
3D world
2D image

## Slide 14: Projection can be tricky…
Slide source: Seitz

## Slide 15: Projection can be tricky…
Slide source: Seitz

## Slide 16: Projective Geometry
What is lost?
Length
Which is closer?
Who is taller?

## Slide 17: Length is not preserved
Figure by David Forsyth
B’
C’
A’

## Slide 18: Projective Geometry
What is lost?
Length
Angles
Perpendicular?
Parallel?

## Slide 19: Parallel lines are not parallel in the image
Figure by David Forsyth

## Slide 20: Projective Geometry
What is preserved?
Straight lines are still straight

## Slide 21: Vanishing points and lines
Parallel lines in the world intersect in the image at a “vanishing point”
Notes: Go to board, sketch out various properties of vanishing points/lines

## Slide 22: Vanishing points and lines
o
Vanishing Point
o
Vanishing Point
Vanishing Line
Notes: Go to board, sketch out various properties of vanishing points/lines
Parallel lines intersect at a point
The intersection of red lines and blue lines form a parallelogram
Sets of parallel lines on the same plane form a vanishing line
Sets of parallel planes form a vanishing line
Not all lines that intersect are parallel

## Slide 23: Vanishing points and lines
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)
Credit: Criminisi

## Slide 24: Vanishing points and lines
Photo from online Tate collection
Notes: Where are the vanishing points? Do buildings on left and buildings on right have the same vanishing line? Which way is the camera tilted?

## Slide 25: Note on estimating vanishing points
Use multiple lines for better accuracy
… but lines will not intersect at exactly the same point in practice
One solution: take mean of intersecting pairs
… bad idea!
Instead, minimize angular differences
Notes: Go to board, sketch out various properties of vanishing points/lines

## Slide 26: (more vanishing points on board)

## Slide 27: Vanishing objects

## Slide 28: Camera matrix
http://www.youtube.com/watch?v=6KlJzfsAzoY
Notes: P = K [R t]

## Slide 29: Projection: world coordinatesimage coordinates
Camera Center (tx, ty, tz)
.
.
.
f
Z
Y
.
Optical Center (u0, v0)
v
u

## Slide 30: Homogeneous coordinates
Conversion
Converting to homogeneous coordinates
homogeneous image
coordinates
homogeneous scene
coordinates
Converting from homogeneous coordinates
Notes: Append coordinate with value 1; proportional coordinate system

## Slide 31: Homogeneous coordinates
Invariant to scaling
Point in Cartesian is ray in Homogeneous
Homogeneous Coordinates
Cartesian Coordinates
Notes: Q: Suppose we have a point in Cartesian coordinates. What is that in homogeneous coordinates? A: a ray

## Slide 32: Basic geometry in homogeneous coordinates
Line equation: ax + by + c = 0
Append 1 to pixel coordinate to get homogeneous coordinate
Line given by cross product of two points
Intersection of two lines given by cross product of the lines

## Slide 33: Work out at home
Write the equation for a line in 2d and 3d using homogeneous coordinates
Why is this the cross product?
Write the equation for a plane in 3D using homogeneous coordinates

## Slide 34: Another problem solved by homogeneous coordinates
  Cartesian: (Inf, Inf)
  Homogeneous: (1, 1, 0)
Intersection of parallel lines
  Cartesian: (Inf, Inf)
Homogeneous: (1, 2, 0)
Notes: Parallel lines intersect at different infinities

## Slide 35
Slide Credit: Saverese
Projection matrix
x: Image Coordinates: w(u,v,1)
K: Intrinsic Matrix (3x3)
R: Rotation (3x3)
t: Translation (3x1)
X: World Coordinates: (X,Y,Z,1)
Ow
iw
kw
jw
R,T

## Slide 36
K
Slide Credit: Saverese
Projection matrix
Intrinsic Assumptions
Unit aspect ratio
Principal point at (0,0)
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Notes: Work through equations for u and v on board

## Slide 37: Remove assumption: known optical center
Intrinsic Assumptions
Unit aspect ratio
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 38: Remove assumption: square pixels
Intrinsic Assumptions
No skew
Extrinsic Assumptions
No rotation
Camera at (0,0,0)

## Slide 39: Remove assumption: non-skewed pixels
Intrinsic Assumptions
Extrinsic Assumptions
No rotation
Camera at (0,0,0)
Note: different books use different notation for parameters

## Slide 40: Oriented and Translated Camera
Ow
iw
kw
jw
t
R

## Slide 41: Allow camera translation
Intrinsic Assumptions
Extrinsic Assumptions
No rotation

## Slide 42: 3D Rotation of Points
Rotation around the coordinate axes, counter-clockwise:
p
p’
g
y
z
Slide Credit: Saverese

## Slide 43: Allow camera rotation

## Slide 44: Degrees of freedom
5
6
Notes: How many known points are needed to estimate this?

## Slide 45: Vanishing Point = Projection from Infinity

## Slide 46: Orthographic Projection
Special case of perspective projection
  Distance from the COP to the image plane is infinite
  Also called “parallel projection”
  What’s the projection matrix?
Image
World
Slide by Steve Seitz

## Slide 47: Scaled Orthographic Projection
Special case of perspective projection
  Object dimensions are small compared to distance to camera
  Also called “weak perspective”
  What’s the projection matrix?
Slide by Steve Seitz
Illustration from George Bebis

## Slide 48: Take-home question
Suppose we have two 3D cubes on the ground facing the viewer, one near, one far.
What would they look like in perspective?
What would they look like in weak perspective?
Photo credit: GazetteLive.co.uk

## Slide 49: Beyond Pinholes: Radial Distortion
Image from Martin Habbecke
Corrected Barrel Distortion

## Slide 50: Things to remember
Vanishing points and vanishing lines
Pinhole camera model and camera projection matrix
Vanishing
point
Vanishing
line
Vanishing
point
Vertical vanishing
point
(at infinity)

## Slide 51: Making pinhole cameras
Groups of 1-2 – find a partner with a good digital camera
http://en.wikipedia.org/wiki/Anaglyph_3D
From James Hays